Ecological building
Basic principles
Buildings more in harmony with nature

---
Not about...

---
Why?
→ Energy crisis
→ Environmental crisis (CO2 emission, toxicity, exploitation, transport, etc.)
→ Obtaining materials (local, cheap…)
→ Doing it yourself with people you can form (exchanges of knowledge, etc.)
→ Live healthier...

---
Definitions

---
Definitions
Building
Constraint
Accommodation
Protection
Must meet structural constraint, thermal, sound, humidity and air renewal constraints.
Allow the reception of people, their goods and their activities.
Weather protection for people, goods and activities.

---
Definitions
Ecological
Ecological
Environmental
Healthy
Materials that return to the earth.
Building interacting with its surrounding through its incoming or outgoing flows (water, energy, air, etc.)
Visually blends into its surroundings.
Made with local materials.
Made with healthy materials (on toxicological and ecotoxicological terms).

---
Steps
Thinking, inspiration, research
Flows to integrate
Construction
Theoretical design
Planning (date, season, material steps, people...)

---
Thinking, inspiration, research

---
Theoretical design

---
Criteria
Definition
Passive
Adapted
Efficient
Sun capture, Trombe wall, insulation, cold room, drying corridor, Canadian wells...
Wind, sun, vegetation, climate, surrounding material...
Devices, compact house, CMV or natural ventilation, heat pump...
The refusal of certain devices can also be taken into account.

---
Compact
The S/V coefficient

---
Criteria
Sun (Light and Heat)
Position of the sun
Window orientation	Window area/floor area ratio
South	20 to 35%
East and West	10 to 25%
North	0 to 10%
Room position workshop.
Interior light
Skylights / Light colors / Window
Sunshine
Trees, neighborhood and other obstacles

---
Criteria
Insulation
Insulation and thermal bridge
Best insulator is not matter, but air. (Contained in straw, coarse elements… unlike finishing coats)
Depending on the material
Felt temperature
The temperature "felt" by the human body is not the temperature of the air. It is an average between this temperature and that of the surrounding walls.
cm equivalent
Thermal bridge
To be limited.

---
Criteria
Humidity
Rate
Between 30 to 70%
Too low : dries out the respiratory mucous membranes which no longer play their filtering role against dust and pathogenic germs.
Too strong disturbs the body's thermo-regulation because evaporation on the surface
of the skin is no longer done, which increases perspiration.
Air renewal is important.

---
Criteria
Consider function
Materials
Functions
Impacts
Thermal inertia / thermal insulating quality / acoustic performance / hygroscopic / bearing capacity / aesthetics ...
Energy / transport / recyclability / toxicity (on humans and the environment)...

---
Flows
Heat and cold, water, waste (including toilets), air, consumption of electrical appliances

---
Criteria
Flows
Cold
Heat
Preservation and alternative methods.
Heat rises.
Convection, conduction, radiation.
Thermodynamics of fluids...
All flows
Limitation of use, origin and treatment.
Deconstruct the uses and solutions for each use.
Think about source type and treatment.
Think about function, not typology.

---
Construction
From the foundations to the roof

---
01
The foundations
Drainage, bearing (permanent load and temporary overload), horizontality

---
Cyclopean Foundation

---
Hemp / bamboo / lime / straw foundation

---
Bedrock

---
02
The slab
Bearing (permanent load and temporary overload), horizontality, thermal

---
Slab

---
03
The lower section
Bearing (permanent load and temporary overload), horizontality, phonic, thermal, aesthetic, hygroscopic, capillary action

---
Lower section

---
04
The walls
Bearing (permanent load and temporary overload), verticality, soundproofing, thermal, aesthetic, hygroscopic

---
Straw wall

---
05
The openings
Brightness (size and opacity), insulation (thermal, sound), aesthetics

---
Bottle wall

---
06
The roof
Protection, bearing (permanent load and temporary overload), phonic, thermal, aesthetic, hygroscopic

---
Reciprocal roof

---
07
Around
Ventilation, thermal, flows treatments...

---
Cardboard furniture

---
Rocket stove

---
Phyto-purification

---
Template
Yellow Idea Template for LibreOffice Impress.
@ealita.id, 2020
Pictures
Book
Under various free licenses,
links on pictures.
La maison des Negawatts |Terre vivante
Content
De la graine à l’humus, Creative Commons CC0.
https://www.graineahumus.org/

---
THANK YOU